## Slide 1: FAFNIR: Accelerating Sparse Gathering by Using Efficient Near-Memory Intelligent Reduction
Junseo Lee
Electrical and Computer Engineering
Seoul National University

## Slide 2: Table of Contents
What is Recommendation System?
Example of Recommendation System: DLRM
Bottleneck of Recommendation System: Embedding layer
Brief Description of State-of-the-Art Solutions of Embedding
  Compositional embedding
  Tensor Casting
FAFNIR
  Challenges of prior solutions
  Comparison with prior solutions
  Contributions
  Evaluation
Question
Conclusion

## Slide 3: What is Recommendation System?
Goal: Predict the "rating" or "preference" a user would give to an item
Example: YouTube, Netflix recommendation system, Facebook DLRM

## Slide 4: What is Recommendation System?
Collaborative filtering
  If someone similar to you likes this item, you are likely to prefer the item either.
Matrix factorization
  “Factorize” a user-item matrix into user & item embedding vectors (=latent factors)
  Good for “sparse” data (lack of data)
  One of the methods of matrix factorization is SVD (singular value decomposition), but not good for sparse user-item matrix

## Slide 5: Example of Recommendation System: DLRM
DLRM = Deep Learning Recommendation System (Facebook)
Sparse feature (categorical data) → Embedding layer
  e.g., watch history, location (country)
Dense feature (continuous data) → MLP (Multilayer Perceptron)
  e.g., watch time, time since last watch

## Slide 6: Embedding Table
One-hot encoding
  One categorical data can be represented as one-hot vector
  This is not a semantic feature
  To use meaningful data for ML, one-hot vector should be converted to the feature which has its own characteristics
Embedding vector (latent factor)
  Semantic feature representing categorical data mapped to latent factor space
  The distance of two vectors in the latent factor space means the similarity of two features
  e.g., King – Queen
  = Man – Woman

## Slide 7: Embedding Table
Problems of embedding layer: Memory intensive operation
  Require high memory capacity
    Tens of MBs to several GBs
    The number of embedding tables varies from 4 to 40
  Irregular memory accesses
    Low cache hit rate
      On an Intel Broadwell server present in production data centers, this results in a high LLC cache miss rate.
      LLC cache miss rate of 8 MPKI (in production-scale recommendation model) compared to 0.5 MPKI, 0.2 MPKI, and 0.06 MPKI in an RNN, FC, and CNN layers
      It result in TLB miss handling cost and prefetching pollution
  Low memory bandwidth utilization
    Prior solutions for embedding layer problem do not fully utilize the memory bandwidth

## Slide 8: Bottleneck of Recommendation System: Embedding layer
SparseLengthsSum(SLS) is embedding operator in Caffe2
RM1, 2 are two representative recommendation models in Facebook’s production datacenter
  RM1 is a comparatively smaller model with few embedding tables; RM2 has tens of embedding tables
  Reference: The Architectural Implications of Facebook's DNN-Based Personalized Recommendation (HPCA ’20)
Operator latency: SLS(embedding layer) > FC > Others

## Slide 9: Solutions of Memory-Intensive Embedding
Compositional embedding
  Reduce the size of embedding table
  Operation-based: concatenation, addition, element-wise multiplication
  Path-based: linear function, MLP
  Partition
    Quotient-Remainder complementary partitions
    Generalized Quotient-Remainder complementary partitions
    Chinese remainder partitions
    Naïve partition

## Slide 10: Solutions of Memory-Intensive Embedding
Compositional embedding (cont’d)
  Partition (emb = embedding table)
    Quotient-Remainder complementary partitions (2 embs)
    Generalized Quotient-Remainder complementary partitions ( embs)
    Chinese remainder partitions ( embs)
    Naïve partition (1 emb)
  Tradeoff: Model accuracy vs. Memory requirement (capacity, bandwidth)

## Slide 11: Solutions of Memory-Intensive Embedding (cont’d)
Tensor Casting (HPCA ’21)
  Target: Backpropagation stage of embedding layer
  Contribution
    Gradient expand-coalesce operation is a bottleneck of backpropagation stage
    Cast gradient expand-coalesce to tensor gather-reduce because it is just inverse process of gather-reduce operation

## Slide 12: Solutions of Memory-Intensive Embedding (cont’d)
Tensor Casting (HPCA ’21) (cont’d)

## Slide 13: Solutions of Memory-Intensive Embedding (cont’d)
Tensor Casting (HPCA ’21) (cont’d)

## Slide 14: FAFNIR
Challenges of prior solutions
  Data movement
    (# queries) x (# vectors in a query) x (vector size) elements must be transferred from memory systems to cores: Memory bandwidth problem
    Goal: reduce the amount of data movement
  Lack of utilization of row buffer locality
    TensorDIMM
      column-major order, which breaks the row-buffer locality in the DRAM system
      splitting embedding vectors across more ranks causes poor utilization of row-buffers
  Relying on spatial locality
    RecNMP
      If low spatial locality, parallel compute at NDP is low compared to that of in theory, DIMM-level parallelsim X
  Connection overhead
    # of connections (𝑐 x 𝑚) is not scalable for adding more ranks
  Using cache to reduce memory access is not a good solution 
    RecNMP: 128KB rank-level cache adds extra HW overhead but hit rate is ~50%

## Slide 15: FAFNIR
Comparison with prior solutions

## Slide 16: FAFNIR
Contribution
  Reduction tree & few connections
    Guarantee that all embedding vectors in a query are definitely reduced within the tree at NDP, so only reduced vectors need to be transferred
    Scalable # of connections: 𝑐 x 𝑚 →
  DIMM-level parallelism
    The performance scales as adding more ranks or increasing batch size
  Effective memory-access reduction
    Only the unique memory accesses in a batch
    No caching mechanism which is less effective (low hit rate)
  Genericity
    Applicable to other sparse problems (sparse gathering)
    e.g., Sparse Matrix-Vector Multiplication (SpMV)

## Slide 17: FAFNIR
Reduction Tree
  2 channels, 8 DIMMs / channel, 2 ranks / DIMM
  4 DIMM/rank nodes, 1 channel node
  7 PEs per DIMM/rank node
Cache size(RecNMP): 128KB
Buffer size: 129.5KB for B=32 ?

## Slide 18: FAFNIR
Reduction Tree (cont’d)
  Indices: concatenation of the index within table and a table number (assumption)
  e.g., 50 = index 5 from table 0

## Slide 19: FAFNIR
Reduction Tree (cont’d)
  (b): "remaining indices" of queries containing "Inx" (unique set of indices)
  e.g., Query a and c have index 11 → queries of headers = a(32, 83, 77) + c(50, 94, 26)
  (c): reduce = if there is a query among B[x].queries which is same as A[i].indices, do reducing
    out.indices = concat(A[i].indices, B[x].indices)
    out.queries = exclude(B[x].queries, A[i].indices) (= B[x].queries - A[i].indices)
  e.g., out.indices = concat(11, 50), out.queries = exclude([11, 94, 26], 11)

## Slide 20: FAFNIR
Effective memory-access reduction
  Only the unique memory accesses in a batch

## Slide 21: FAFNIR
Genericity
  Applicable to other sparse problems (sparse gathering)
  SpMV
    Main difference: embedding - vectors → one vector, SpMV – vector → element
    Vectorization: gathering non-zero elements in sparse matrix as continuous vectors

## Slide 22: FAFNIR
Evaluation
  Experimental setup
  Sparse matrices
    Six from the scientific domain
    Six graphs

## Slide 23: FAFNIR
Evaluation
  Scalability according to batch size & # of ranks
    (a): RecNMP, (b): Fafnir

## Slide 24: FAFNIR
Evaluation
  SpMV: Speedup over baseline (Two-Step algorithm)

## Slide 25: FAFNIR
Evaluation
  Resource utilization & Power consumption
    FPGA utilization: LUT – ~5%, LUTRAM – ~0.15%, FF – ~1%, BRAM – ~13%
    Power consumption (FPGA)
      Fafnir: DIMM/rank nodes - 0.23mW, channel node – 0.18W (in total, FPGA)
      Uniform distribution, no hot spot (ASIC)

## Slide 26: FAFNIR
Evaluation
  Power consumption & Area overhead
    Power consumption (ASIC)
      PE: 10.82mW, DIMM/rank node: 23.82mW, Channel node: 16.37mW
      Fafnir: 111.65mW << one DDR4 DIMM: 13W
    Area overhead
      Benefit of embedding PEs into one chip (instead of distributing across DIMMs)
      0.282 < 0.077 * 7 = 0.539
      Total area comparison: 0.282 * 4 + 0.121 = 1.249 < 8.64 (RecNMP)

## Slide 27: FAFNIR
Questions
  How to apply Fafnir to weighted embedding lookup?
    Even if the embedding vector is shared by queries, the weight of the vector would be different
    PyTorch: nn.EmbeddingBag – compute sum (or other operations) of ‘bags’ of embeddings with no intermediate embeddings (abstraction)
    Code from DLRM: nn.EmbeddingBag instantiation

## Slide 28: Conclusion
Recommendation system is a hot topic in system/ML groups
Embedding lookup is the main bottleneck which is memory- intensive operation compared to DNN/RNN which are compute-intensive
FAFNIR is the one of architectural solutions which utilizes a reduction tree
  Unique memory access
  Scalable memory interconnection
  Genericity